## Slide 1: A Review of Published Work Relating to Remote Sensing of Vegetative Cover With LiDAR

## Slide 2: Overview
Influence of Vegetation Structure on Lidar-derived Canopy Height and Fractional Cover in Forested Riparian Buffers During Leaf-Off and Leaf-On Conditions / Quantifying land use effects on forested riparian buffer vegetation structure using LiDAR data
  Wasser, Chasmer, Day and Taylor, 2013 / 2015
Extensive Riparian Vegetation Monitoring – Remote Sensing Pilot Study
  Moskal, Cooke, Axe and Comnick, 2017
LiDAR measurement of sagebrush steppe vegetation heights
  Struetker and Glenn, 2006
Integrating LIDAR data and multispectral imagery for enhanced classification of rangeland vegetation: A meta analysis
  Bork and Su, 2007
Fusion of LiDAR and imagery for estimating forest canopy fuels
  Erdody and Moskal, 2010
Estimation of canopy cover in dense mixed-species forests using airborne lidar data
  Arumae and Lang, 2017
Improving representation of riparian vegetation shading in a regional stream temperature model using LiDAR data
  Loicq et al., 2018
Mapping Riparian Vegetation Functions Using 3D Bispectral LiDAR Data
  Ladlier, Hubert-Moy and Dufour, 2019
Automated Individual Tree Measurement Through Morphological Analysis of a LIDAR-Based Canopy Surface Model
  Andersen, Reutebuch and Scheruder, 2001, presented at The Proceedings of the First International Precision Forestry Cooperative Symposium

## Slide 3: Synopsis

## Slide 4: Influence of Vegetation Structure on Lidar-derived Canopy Height and Fractional Cover in Forested Riparian Buffers During Leaf-Off and Leaf-On Conditions / Quantifying land use effects on forested riparian buffer vegetation structure using LiDAR data Wasser, Chasmer, Day and Taylor, 2013 / 2015, PLOS One / Ecosphere
175 sq mi watershed in central PA
Used 80 circular plots (r=11.3m) to validate veg. estimates
Looking specifically to estimate fractional canopy cover
Favored “vertical height percentiles” over gridded canopy height models for constructing canopy height
Used an automated method to determine buffer width

## Slide 5: Extensive Riparian Vegetation Monitoring – Remote Sensing Pilot Study Moskal, Cooke, Axe and Comnick, 2017, Produced for WA DENR?
Propose methods for using LiDAR to assess:
  Canopy Height (well studied)
  Canopy Percent Cover (well studied)
  Stand Density (worked well)
  Conifer/Deciduous Classification (did not work well)
  Vegetation Class/Seral Stage (unknown how accurate)
  Species ID (assumed to be near-impossible)

## Slide 6: LiDAR measurement of sagebrush steppe vegetation heights Struetker and Glenn, 2006, Remote Sensing of Environment
Used surface roughness of DHMs to differentiate burned from unburned vegetation

## Slide 7: Integrating LIDAR data and multispectral imagery for enhanced classification of rangeland vegetation: A meta analysis Bork and Su, 2007, Remote Sensing of Environment
Aspen Parkland of western Canada
Used LiDAR collected w/ simultaneous RGB imagery
Tried classifying imagery using 3 or 8 classes
  Imagery alone: 75% / 59% accuracy
  LiDAR alone: 65% / 52% accuracy
  Combined: 91% / 80% accuracy
Model appears to be very specialized for study area
  A lot of human model input that would need to be changed for different study areas