## Slide 1: A Review of Published Work Relating to Remote Sensing of Vegetative Cover With LiDAR

## Slide 2: Overview
Influence of Vegetation Structure on Lidar-derived Canopy Height and Fractional Cover in Forested Riparian Buffers During Leaf-Off and Leaf-On Conditions / Quantifying land use effects on forested riparian buffer vegetation structure using LiDAR data
  Wasser, Chasmer, Day and Taylor, 2013 / 2015
Extensive Riparian Vegetation Monitoring – Remote Sensing Pilot Study
  Moskal, Cooke, Axe and Comnick, 2017
LiDAR measurement of sagebrush steppe vegetation heights
  Struetker and Glenn, 2006
Integrating LIDAR data and multispectral imagery for enhanced classification of rangeland vegetation: A meta analysis
  Bork and Su, 2007
Fusion of LiDAR and imagery for estimating forest canopy fuels
  Erdody and Moskal, 2010
Improving representation of riparian vegetation shading in a regional stream temperature model using LiDAR data
  Loicq et al., 2018
Mapping Riparian Vegetation Functions Using 3D Bispectral LiDAR Data
  Ladlier, Hubert-Moy and Dufour, 2019
Automated Individual Tree Measurement Through Morphological Analysis of a LIDAR-Based Canopy Surface Model
  Andersen, Reutebuch and Scheruder, 2001, presented at The Proceedings of the First International Precision Forestry Cooperative Symposium

## Slide 3: Influence of Vegetation Structure on Lidar-derived Canopy Height and Fractional Cover in Forested Riparian Buffers During Leaf-Off and Leaf-On Conditions / Quantifying land use effects on forested riparian buffer vegetation structure using LiDAR data Wasser, Chasmer, Day and Taylor, 2013 / 2015, PLOS One / Ecosphere
175 sq mi watershed in central PA
Used 80 circular plots (r=11.3m) to validate veg. estimates
Looking specifically to estimate fractional canopy cover
Favored “vertical height percentiles” over gridded canopy height models for constructing canopy height
Used an automated method to determine buffer width

## Slide 4: Extensive Riparian Vegetation Monitoring – Remote Sensing Pilot Study Moskal, Cooke, Axe and Comnick, 2017, Produced for WA DENR?
Propose methods for using LiDAR to assess:
  Canopy Height (well studied)
  Canopy Percent Cover (well studied)
  Stand Density (worked well)
  Conifer/Deciduous Classification (did not work well)
  Vegetation Class/Seral Stage (unknown how accurate)
  Species ID (assumed to be near-impossible)

## Slide 5: LiDAR measurement of sagebrush steppe vegetation heights Struetker and Glenn, 2006, Remote Sensing of Environment
Used surface roughness of DHMs to differentiate burned from unburned vegetation

## Slide 6: Integrating LIDAR data and multispectral imagery for enhanced classification of rangeland vegetation: A meta analysis Bork and Su, 2007, Remote Sensing of Environment
Aspen Parkland of western Canada
Used LiDAR collected w/ simultaneous RGB imagery
Tried classifying imagery using 3 (forest, shrubs, grass) or 8 classes
  Imagery alone: 75% / 59% accuracy
  LiDAR alone: 65% / 52% accuracy
  Combined: 91% / 80% accuracy
Model appears to be very specialized for study area
  A lot of human model input that would need to be changed for different study areas

## Slide 7: Fusion of LiDAR and imagery for estimating forest canopy fuels Erdody and Moskal, 2010, Remote Sensing of Environment
Tried to estimate the mass density distribution of a forest

## Slide 8: Improving representation of riparian vegetation shading in a regional stream temperature model using LiDAR data Loicq et al., 2018, Science of the Total Environment
Could shading estimates be of any interest to us?
Otherwise nothing much of interest

## Slide 9: Mapping Riparian Vegetation Functions Using 3D Bispectral LiDAR Data Ladlier, Hubert-Moy and Dufour, 2019, Water
Functions evaluated:
  Canopy Height
  STDDEV of Canopy Height
  Vertical Canopy Structure (used n_first_returns/n_returns as proxy for canopy density)
  Area and Volume of Vegetation Overhanging River
  Trees Species Composition (Supervised ML)
  Density of Herbaceous Stratum (Supervised ML)
  Density of Shrub Stratum (Supervised ML)
  Number of Trunks (Supervised ML)
The functions evaluated with ML were evaluated on discrete intervals (rather than continuous)

## Slide 10: Automated Individual Tree Measurement Through Morphological Analysis of a LIDAR-Based Canopy Surface Model Andersen, Reutebuch and Scheruder, 2001, presented at The Proceedings of the First International Precision Forestry Cooperative Symposium
An interesting discussion of mathematical morphology and image processing as it related to canopy analysis
Can use morphological transformations to measure individual trees using LiDAR

## Slide 11: Synopsis
Attempts have been made to evaluate vegetation cover type
Generalizable models seem understudied
  Detailed canopy classification models either use hand-picked classification parameters that seem unlikely to generalize to other study areas, or use supervised ML algorithms that need to be trained
  No models evaluated against dissimilar study areas
None of these papers have packaged their workflow into downloadable software/modules/etc.
LiDAR-only models that try to differentiate vegetation classes are low accuracy (~60%) even within the study area they were built for

## Slide 12: Going Forward
A general model for riparian cover classification has not been published yet
  Could use several study areas to train and optimize a general model
  Model building could use supervised ML and optimization
  But final model shouldn’t use supervised ML (could use raster math, unsupervised ML)
This model could also be packaged for distribution (e.g., a Python package)
  Such a distribution could also incorporate ideas from other papers